RPI M30A

High efficiency 3-phase solar inverters for the European market - Perfect choice for large-scale solar PV systems, such as those used in the commercial or agricultural sectors.

Versatile applications

●	Aluminium housing ensures long lasting protection against moisture and corrosion

●    Wide input voltage range

●	Suitable for indoor and outdoor applications (IP65)

Maximum proﬁtability

●    Peak efficiency of 98.5 %

●	2 MPP trackers for increased ﬂexibility and maximum yield

●	Symmetrical and asymmetrical loading possible (33/67 %)

●	Nominal apparent power 30 kVA (33 kVA max. apparent power possible 4))

www.solar-inverter.com

30 kVA transformerless solar inverters

Technical data RPI M30A

INPUT (DC)                              RPI M30A

Max. recommended PV

power                                       38 kWP

Max. input power                      35 kW Nominal power                         31.5 kW 2) Voltage range                           200 ... 1000 V MPP operating voltage

SAFETY / STANDARDS          RPI M30A

Protection degree                     IP65

Safety class                              I Configurable trip parameters   Yes Insulation monitoring                Yes

Overload behavior                    Current limitation; power limitation

range                                        200 ... 1000 V

Startup voltage                         250 V

Anti-islanding protection / Grid regulation

VDE 0126-1-1/A1; UTE C15-712-1

VDE 16 1-1 A1 VFR 2013/VFR 2014; VDE-AR-N 4105; BDEW

Voltage range for

maximum power                       520 ... 800 V with symmetrical load (50/50 %)

Max. current                             60 A (30 A per MPP tracker)

EMC	EN61000-6-2; EN61000-6-3; EN61000-3-11; EN61000-3-1

Safety                                       IEC62109-1 / -2; CE conformity

Max. number of

MPP trackers

Parallel inputs: 1 MPP tracker

Separate inputs: 2 MPP trackers

1)   When operated with symmetrical DC inputs (50/50 %)

2)   Maximum 21 kW per DC input with asymmetrical load

Input load                                 ≤ 21 kW per MPP tracker; symmetrical and asymmetrical

OUTPUT (AC)

Max. apparent power                33 kVA 3)  4)

Nominal apparent power          30 kVA 3)

Voltage range                           230 V ± 10% / 400 V ± 10 % 5)

3 phase + PE or 3 phase + N + PE

Nominal current                        43.5 A Nominal frequency                   50 / 60 Hz Frequency range                      50 / 60 Hz ± 5 Hz 5) Power factor adjustable            0.8 cap ... 0.8 ind Total harmonic distortion

(THD)                                       < 3 % @ nominal apparent power

3)   Cos Phi = 1 (VA = W)

4)   33 kVA / 48 A AC is possible under the following conditions: DC input voltage > 580 V with symmetrical load and ambient temp. is < 40 °C.

5)   AC voltage and frequency range will be programmed according to the individual country requirements.

GENERAL SPECIFICATION

Model name                             RPI M30A_121

Part number Delta                    RPI303FA0E1100

Max. efficiency                         98.5 % Efficiency EU                            98.2 % Operating temperature             -25 ... +60 °C Full power without derating      -25 ... +40 °C Storage temperature                -25 ... +60 °C

Humidity                                   0 ... 100 % non-condensing

Max. operating altitude             2000 m (above sea level)

Standard guarantee                 5 years (guarantee extension is possible)

MECHANICAL DESIGN

Size (L x W x D)                       625 x 612 x 278 mm

Weight                                      48.5 kg

Cooling                                     Fans

AC connector                           China Aviation Optical-Electrical Technology Co.

PVE5T50KP73 (included)

DC connector                           6 pairs Multi-Contact MC4 (included) Communication interfaces       2 x RS485, 2 x Dry contacts, 1 x EPO, 6 x Digital

inputs

AC/DC disconnector                Integrated

Display                                     2 LEDs, 4-line LCD

United Kingdom

Email:    sales.uk@solar-inverter.com

Tel:        0800 051 4280 (Free Call)

International

Email:    sales.europe@solar-inverter.com

Tel:        +49 7641 455 547

www.solar-inverter.com

May 23, 2015 - All information and specifications are subject to change without notice

# Text boxes

1)