/ Perfect Welding / Solar Energy / Perfect Charging

Fronius symo

/ Maximum flexibility for the applications of tomorrow.

N

W                           E

/ SnapINverter technology

/ Integrated data communication

S

/ SuperFlex

Design

/ Dynamic Peak

Manager

/ Smart Grid

Ready

/ Boasting power categories ranging from 3.0 to 20.0 kW, the transformerless Fronius Symo is the three-phase inverter for systems of every size. Owing to the SuperFlex Design, the Fronius Symo is the perfect answer to irregularly shaped or multi-oriented  roofs. The standard  interface to the internet  via WLAN or Ethernet  and the ease of integration  of third-party components make the Fronius Symo one of the most communicative inverters on the market. Furthermore,

the meter interface permits dynamic feed-in management  and a clear visualisation of the consumption  overview.

TECHNICAL DATA FRONIUS  SYMO (3.0-3-S, 3.7-3-S, 4.5-3-S, 3.0-3-M, 3.7-3-M, 4.5-3-M)

| INPUT DATA | SYMO 3.0-3-S | SYMO 3.7-3-S | SYMO 4.5-3-S | SYMO 3.0-3-M | SYMO 3.7-3-M | SYMO 4.5-3-M |
| --- | --- | --- | --- | --- | --- | --- |
| Max. input current (Idc max 1 / Idc max 2 1)) Max. array short circuit current (MPP1/MPP2 1)) Min. input voltage (Udc min) Feed-in start voltage (Udc start) Nominal input voltage (Udc,r) Max. input voltage (Udc max) MPP voltage range (Umpp min – Umpp max) | 16.0 A / 16.0 A 24.0 A / 24.0 A 150 V 200 V 595 V 1,000 V |
|  | 200 - 800 V | 250 - 800 V | 300 - 800 V | 150 - 800 V |
| Number MPP trackers | 1 | 2 |
| Number of DC connections | 3 | 2+2 |

| OUTPUT DATA | SYMO 3.0-3-S | SYMO 3.7-3-S | SYMO 4.5-3-S | SYMO 3.0-3-M | SYMO 3.7-3-M | SYMO 4.5-3-M |
| --- | --- | --- | --- | --- | --- | --- |
| AC nominal output (Pac,r) | 3,000 W | 3,700 W | 4,500 W | 3,000 W | 3,700 W | 4,500 W |
| Max. output power | 3,000 VA | 3,700 VA | 4,500 VA | 3,000 VA | 3,700 VA | 4,500 VA |
| AC output current (Iac nom) Grid connection (voltage range) Frequency (Frequency range) Total harmonic distortion Power factor (cos φac,r) | 4.3 A | 5.3 A | 6.5 A | 4.3 A | 5.3 A | 6.5 A |
|  | 3~NPE 400 V / 230 V or 3~NPE 380 V / 220 V (+20 % / -30 %) 50 Hz / 60 Hz (45 - 65 Hz) < 3 % 0.70 - 1 ind. / cap. 0.85 - 1 ind. / cap. |

GENERAL DATA                                                       SYMO  3.0-3-S     SYMO 3.7-3-S     SYMO 4.5-3-S     SYMO 3.0-3-M    SYMO 3.7-3-M    SYMO 4.5-3-M

Dimensions (height x width x depth)                                                                                                                   645 x 431 x 204 mm

Weight                                                                                                                        16.0 kg                                                                                                 19.9 kg

Degree of protection                                                                                                                                                            IP 65

Protection class                                                                                                                                                                      1

Overvoltage category (DC / AC) 2)                                                                                                                                                                                                                                                            2 / 3

Night time consumption                                                                                                                                                     < 1 W Inverter design                                                                                                                                                           Transformerless Cooling                                                                                                                                                                   Regulated air cooling

Installation                                                                                                                                                     Indoor and outdoor installation

Ambient temperature  range                                                                                                                                          -25 -  +60 °C Permitted humidity                                                                                                                                                         0 -  100 %

Max. altitude                                                                                                                            2,000 m / 3,400 m (unrestricted / restricted voltage range)

DC connection technology                                                       3x DC+ and 3x DC- screw terminals 2.5 - 16 mm²                            4x DC+ and 4x DC- screw terminals 2.5 - 16mm2 3)

AC connection technology                                                              5-pole AC screw terminals  2.5 - 16 mm²                                           5-pole AC screw terminals 2.5 - 16mm2 3)

Certificates and compliance with standards                     ÖVE / ÖNORM E 8001-4-712, DIN V VDE 0126-1-1/A1, VDE AR N 4105, IEC 62109-1/-2, IEC 62116, IEC 61727, AS 3100, AS 4777-2, AS 4777-3, CER 06-190, G83/2, UNE 206007-1, SI 4777 1), CEI 0-21 1) , NRS 097

1)  This applies to Fronius Symo 3.0-3-M, 3.7-3-M and 4.5-3-M.

2)  According to IEC 62109-1.

3)  16 mm² without wire end ferrules. Further information regarding the availability of the inverters in your country can be found at www.fronius.com.

FRONIUS SYMO 4.5-3-S EFFICIENCY CURVE                                         FRONIUS  SYMO 4.5-3-S TEMPERATURE DERATING

| 100 |  | 5,000 |  |
| --- | --- | --- | --- |
| 98 |  |  |  |
| 96 |  | 4,000 |  |
| 94 |  |  |  |
| 92 |  |  |  |

90

88

86

84

82

0        0.1      0.2      0.3      0.4      0.5      0.6      0.7      0.8       0.9        1

2,000

1,000

0

30                        35                        40                        45                        50

STANDARDISED OUTPUT POWER PAC / PAC,R

■ 300 VDC     ■ 595 VDC     ■ 800 VDC

AMBIENT  TEMPERATURE [°C]

■ 300 VDC    ■ 630 VDC    ■ 800 VDC

TECHNICAL DATA FRONIUS  SYMO (3.0-3-S, 3.7-3-S, 4.5-3-S, 3.0-3-M, 3.7-3-M, 4.5-3-M)

| EFFICIENCY | SYMO 3.0-3-S | SYMO 3.7-3-S | SYMO 4.5-3-S | SYMO 3.0-3-M | SYMO 3.7-3-M | SYMO 4.5-3-M |
| --- | --- | --- | --- | --- | --- | --- |
| Max. efficiency |  |  |  | 98.0 % |  |  |
| European efficiency (ηEU) | 96.2 % | 96.7 % | 97.0 % | 96.5 % | 96.9 % | 97.2 % |
| η at 5 % Pac.r 1) | 80.3 / 83.6 / 79.1 % | 83.4 / 86.4 / 80.6 % | 84.8 / 88.5 / 82.8 % | 79.8 / 85.1 / 80.8 % | 81.6 / 87.8 / 82.8 % | 83.4 / 90.3 / 85.0 % |
| η at 10 % Pac.r 1) | 87.8 / 91.0 / 86.2 % | 90.1 / 92.5 / 88.7 % | 91.7 / 93.7 / 90.3 % | 86.5 / 91.6 / 87.7 % | 87.9 / 93.6 / 90.5 % | 89.2 / 94.1 / 91.2 % |
| η at 20 % Pac.r 1) | 92.6 / 95.0 / 92.6 % | 93.7 / 95.7 / 93.6 % | 94.6 / 96.3 / 94.5 % | 90.8 / 95.3 / 93.0 % | 91.9 / 96.0 / 94.1 % | 92.8 / 96.5 / 95.1 % |
| η at 25 % Pac.r 1) | 93.4 / 95.6 / 93.8 % | 94.5 / 96.4 / 94.7 % | 95.2 / 96.8 / 95.4 % | 91.9 / 96.0 / 94.2 % | 92.9 / 96.6 / 95.2 % | 93.5 / 97.0 / 95.8 % |
| η at 30 % Pac. 1) | 94.0 / 96.3 / 94.5 % | 95.0 / 96.7 / 95.4 % | 95.6 / 97.2 / 95.9 % | 92.8 / 96.5 / 95.1 % | 93.5 / 97.0 / 95.8 % | 94.2 / 97.3 / 96.3 % |
| η at 50 % Pac.r 1) | 95.2 / 97.3 / 96.3 % | 96.9 / 97.6 / 96.7 % | 96.4 / 97.7 / 97.0 % | 94.3 / 97.5 / 96.5 % | 94.6 / 97.7 / 96.8 % | 94.9 / 97.8 / 97.2 % |
| η at 75 % Pac.r 1) | 95.6 / 97.7 / 97.0 % | 96.2 / 97.8 / 97.3 % | 96.6 / 98.0 / 97.4 % | 94.9 / 97.8 / 97.2 % | 95.0 / 97.9 / 97.4 % | 95.1 / 98.0 / 97.5 % |
| η at 100 % Pac.r 1) | 95.6 / 97.9 / 97.3 % | 96.2 / 98.0 / 97.5 % | 96.6 / 98.0 / 97.5 % | 95.0 / 98.0 / 97.4 % | 95.1 / 98.0 / 97.5 % | 95.0 / 98.0 / 97.6 % |

MPP adaptation efficiency                                                                                                                                      > 99.9 %

1)  And at Umpp min / Udc.r / Umpp max

| PROTECTIVE DEVICES | SYMO 3.0-3-S | SYMO 3.7-3-S | SYMO 4.5-3-S | SYMO 3.0-3-M | SYMO 3.7-3-M | SYMO 4.5-3-M |
| --- | --- | --- | --- | --- | --- | --- |

DC insulation measurement                                                                                                                                         Yes

Overload behaviour                                                                                                                        Operating point shift. power limitation

DC disconnector                                                                                                                                                           Yes

Reverse polarity protection                                                                                                                                          Yes

| INTERFACES | SYMO 3.0-3-S | SYMO 3.7-3-S | SYMO 4.5-3-S | SYMO 3.0-3-M | SYMO 3.7-3-M | SYMO 4.5-3-M |
| --- | --- | --- | --- | --- | --- | --- |

WLAN / Ethernet LAN                                                                                           Fronius Solar.web, Modbus TCP SunSpec, Fronius Solar API (JSON)

6 inputs and 4 digital in/out                                                                                                               Interface to ripple control receiver

USB (A socket) 2)                                                                                                                                                                                                                           Datalogging, inverter update via USB flash drive

2x RS422 (RJ45 socket) 2)                                                                                                                                                                                                                                               Fronius Solar Net

Signalling output 2)                                                                                                                                                                                                                  Energy management  (potential-free relay output) Datalogger and Webserver                                                                                                                                      Included

External input 2)                                                                                                                                                                                                                     S0-Meter Interface / Input for overvoltage protection

RS485                                                                                                                                          Modbus RTU SunSpec or meter connection

2)  Also available in the light version.

TECHNICAL DATA FRONIUS  SYMO (5.0-3-M, 6.0-3-M, 7.0-3-M, 8.2-3-M)

| INPUT DATA | SYMO 5.0-3-M | SYMO 6.0-3-M | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- |
| Max. input current (Idc max 1 / Idc max 2) Max. array short circuit current (MPP1/MPP2) Min. input voltage (Udc min) Feed-in start voltage (Udc start) Nominal input voltage (Udc,r) Max. input voltage (Udc max) MPP voltage range (Umpp min – Umpp max) Number MPP trackers Number of DC connections | 16.0 A / 16.0 A 24.0 A / 24.0 A 150 V 200 V 595 V 1,000 V 163 - 800 V 195 - 800 V 228 - 800 V 267 - 800 V 2 2 + 2 |

| OUTPUT DATA | SYMO 5.0-3-M | SYMO 6.0-3-M | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- |
| AC nominal output (Pac,r) | 5,000 W | 6,000 W | 7,000 W | 8,200 W |
| Max. output power | 5,000 VA | 6,000 VA | 7,000 VA | 8,200 VA |
| AC output current (Iac nom) Grid connection (voltage range) Frequency (Frequency range) Total harmonic distortion Power factor (cos φac,r) | 7.2 A | 8.7 A | 10.1 A | 11.8 A |
|  | 3-NPE 400 V / 230 V or 3~NPE 380 V / 220 V (+20 % / -30 %) 50 Hz / 60 Hz (45 - 65 Hz) < 3 % 0.85 - 1 ind. / cap. |

| GENERAL DATA | SYMO 5.0-3-M | SYMO 6.0-3-M | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- |
| Dimensions (height x width x depth) | 645 x 431 x 204 mm |
| Weight | 19.9 kg | 21.9 kg |
| Degree of protection Protection class Overvoltage category (DC / AC) 1) Night time consumption Inverter design Cooling Installation Ambient temperature range Permitted humidity Max. altitude DC connection technology AC connection technology Certificates and compliance with standards | IP 65 |
|  | 1 2 / 3 < 1 W Transformerless Regulated air cooling Indoor and outdoor installation -25 - +60 °C 0 - 100 % 2,000 m / 3,400 m (unrestricted / restricted voltage range) 4x DC+ and 4x DC- Screw terminals 2.5 - 16mm2 2) 5-pole AC Screw terminals 2.5 - 16mm2 2) ÖVE / ÖNORM E 8001-4-712, DIN V VDE 0126-1-1/A1, VDE AR N 4105, IEC 62109-1/-2, IEC 62116, IEC 61727, AS 3100, AS 4777-2, AS 4777-3, CER 06-190, G83/2, UNE 206007-1, SI 4777, CEI 0-21, NRS 097 |

1)  According to IEC 62109-1.

2)  16 mm² without wire end ferrules.

Further information regarding the availability of the inverters in your country can be found at www.fronius.com.

FRONIUS SYMO 8.2-3-M  EFFICIENCY CURVE                                  FRONIUS  SYMO 8.2-3-M TEMPERATURE DERATING

| 100 |  | 9,000 |  |
| --- | --- | --- | --- |
| 98 |  |  |  |
| 96 |  |  |  |
| 94 |  | 6,000 |  |
| 92 |  |  |  |
| 90 |  |  |  |
| 88 |  | 3,000 |  |
| 86 |  |  |  |
| 84 |  |  |  |
| 82 |  | 0 |  |
|  | 0 0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8 0.9 1 |  | 30 35 40 45 50 |

STANDARDISED  OUTPUT POWER PAC / PAC,R

■ 258 VDC     ■ 595 VDC     ■ 800 VDC

AMBIENT TEMPERATURE [°C]

■ 258 VDC    ■ 595 VDC    ■ 800 VDC

TECHNICAL DATA FRONIUS  SYMO (5.0-3-M, 6.0-3-M, 7.0-3-M, 8.2-3-M)

| EFFICIENCY | SYMO 5.0-3-M | SYMO 6.0-3-M |  | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- | --- |
| Max. efficiency |  |  | 98.0 % |  |  |
| European efficiency (ηEU) | 97.3 % | 97.5 % |  | 97.6 % | 97.7 % |
| η at 5 % Pac,r 1) | 84.9 / 91.2 / 85.9 % | 87.8 / 92.6 / 87.8 % |  | 88.7 / 93.1 / 89.0 % | 89.8 / 93.8 / 90.6 % |
| η at 10 % Pac,r 1) | 89.9 / 94.6 / 91.7 % | 91.3 / 95.6 / 93.0 % |  | 92.0 / 95.9 / 94.7 % | 92.8 / 96.1 / 94.5 % |
| η at 20 % Pac,r 1) | 93.2 / 96.7 / 95.4 % | 94.1 / 97.1 / 95.9 % |  | 94.5 / 97.3 / 96.3 % | 95.0 / 97.6 / 96.6 % |
| η at 25 % Pac,r 1) | 93.9 / 97.2 / 96.0 % | 94.7 / 97.5 / 96.5 % |  | 95.1 / 97.6 / 96.7 % | 95.5 / 97.7 / 97.0 % |
| η at 30 % Pac, 1) | 94.5 / 97.4 / 96.5 % | 95.1 / 97.7 / 96.8 % |  | 95.4 / 97.7 / 97.0 % | 95.8 / 97.8 / 97.2 % |
| η at 50 % Pac,r 1) | 95.2 / 97.9 / 97.3 % | 95.7 / 98.0 / 97.5 % |  | 95.9 / 98.0 / 97.5 % | 96.2 / 98.0 / 97.6 % |
| η at 75 % Pac,r 1) | 95.3 / 98.0 / 97.5 % | 95.7 / 98.0 / 97.6 % |  | 95.9 / 98.0 / 97.6 % | 96.2 / 98.0 / 97.6 % |
| η at 100 % Pac,r 1) | 95.2 / 98.0 / 97.6 % | 95.7 / 97.9 / 97.6 % |  | 95.8 / 97.9 / 97.5 % | 96.0 / 97.8 / 97.5 % |
| MPP adaptation efficiency |  |  | > 99.9 % |  |  |

1)  And at Umpp min / Udc,r / Umpp max

| PROTECTIVE DEVICES | SYMO 5.0-3-M | SYMO 6.0-3-M | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- |
| DC insulation measurement Yes |

Overload behaviour                                                                                                                                     Operating point shift. power limitation

DC disconnector                                                                                                                                                                        Yes

Reverse polarity protection                                                                                                                                                       Yes

| INTERFACES | SYMO 5.0-3-M | SYMO 6.0-3-M | SYMO 7.0-3-M | SYMO 8.2-3-M |
| --- | --- | --- | --- | --- |
| WLAN / Ethernet LAN 6 inputs and 4 digital in/out USB (A socket) 2) 2x RS422 (RJ45 socket) 2) Signalling output 2) Datalogger and Webserver External input 2) RS485 | Fronius Solar.web, Modbus TCP SunSpec, Fronius Solar API (JSON) |
|  | Interface to ripple control receiver Datalogging, inverter update via USB flash drive Fronius Solar Net Energy management (potential-free relay output) Included S0-Meter Interface / Input for overvoltage protection Modbus RTU SunSpec or meter connection |

2) Also available in the light version.

TECHNICAL DATA FRONIUS  SYMO (10.0-3-M, 12.5-3-M, 15.0-3-M, 17.5-3-M, 20.0-3-M)

| INPUT DATA Max. input current (Idc max 1 / Idc max 2) | SYMO 10.0-3-M SYMO 12.5-3-M 27.0 A / 16.5 A 1) | SYMO 15.0-3-M SYMO 17.5-3-M SYMO 20.0-3-M 33.0 A / 27.0 A |
| --- | --- | --- |
| Max. usable input current total (Idc max 1 + Idc max 2) | 43.5 A | 51.0 A |
| Max. array short circuit current (MPP1/MPP2) Min. input voltage (Udc min) Feed-in start voltage (Udc start) Nominal input voltage (Udc,r) Max. input voltage (Udc max) MPP voltage range (Umpp min – Umpp max) Number MPP trackers Number of DC connections | 40.5 A / 24.8 A | 49.5 A / 40.5 A |
|  | 200 V 200 V 600 V 1,000 V 270 - 800 V 320 - 800 V 370 - 800 V 420 - 800 V 2 3+3 |
| Max. PV generator output (Pdc max) 15.0 kWpeak 18.8kWpeak 22.5 kWpeak 26.3 kWpeak 30.0 kWpeak |

| OUTPUT DATA AC nominal output (Pac,r) | SYMO 10.0-3-M 10,000 W | SYMO 12.5-3-M 12,500 W | SYMO 15.0-3-M 15,000 W | SYMO 17.5-3-M 17,500 W | SYMO 20.0-3-M 20,000 W |
| --- | --- | --- | --- | --- | --- |
| Max. output power | 10,000 VA | 12,500 VA | 15,000 VA | 17,500 VA | 20,000 VA |
| AC output current (Iac nom) | 14.4 A | 18.0 A | 21.7 A | 25.3 A | 28.9 A |
| Grid connection (voltage range) |  | 3-NPE 400 V / 230 V or 3~NPE 380 V / 220 V (+20 % / -30 %) |  |
| Frequency (Frequency range) |  | 50 Hz / 60 Hz (45 - 65 Hz) |  |
| Total harmonic distortion | 1.8 % | 2.0 % 1.5 % 1.5 % | 1.3 % |
| Power factor (cos φac,r) |  | 0 - 1 ind. / cap. |  |

| GENERAL DATA Dimensions (height x width x depth) | SYMO 10.0-3-M SYMO 12.5-3-M SYMO 15.0-3-M SYMO 17.5-3-M SYMO 20.0-3-M |
| --- | --- |
|  | 725 x 510 x 225 mm |
| Weight | 34.8 kg | 43.4 kg |
| Degree of protection Protection class Overvoltage category (DC / AC) 2) Night time consumption Inverter design Cooling Installation Ambient temperature range Permitted humidity Max. altitude DC connection technology AC connection technology Certificates and compliance with standards | IP 66 |
|  | 1 2 / 3 < 1 W Transformerless Regulated air cooling Indoor and outdoor installation -40 - +60 °C 0 - 100 % 2,000 m / 3,400 m (unrestricted / restricted voltage range) 6x DC+ and 6x DC- screw terminals 2.5 - 16 mm2 5-pole AC screw terminals 2.5 - 16 mm2 ÖVE / ÖNORM E 8001-4-712, DIN V VDE 0126-1-1/A1, VDE AR N 4105, IEC 62109-1/-2, IEC 62116, IEC 61727, AS 3100, AS 4777-2, AS 4777-3, CER 06-190, G83/2, UNE 206007-1, SI 4777, CEI 0-16, CEI 0-21, NRS 097 |

1) 14.0 A for voltages < 420 V

2) According to IEC 62109-1. DIN rail for optional overvoltage protection (type 2) is included.

Further information regarding the availability of the inverters in your country can be found at www.fronius.com.

FRONIUS SYMO 20.0-3-M EFFICIENCY CURVE                                          FRONIUS  SYMO 20.0-3-M TEMPERATURE DERATING

99

98

97

24,000

20,000

96

95

12,000

93

8,000

92

4,000

91

0        0.1      0.2      0.3      0.4      0.5      0.6      0.7      0.8       0.9        1

0

30                       35                        40                       45                        50

STANDARDISED  OUTPUT POWER PAC / PAC,R

■ 420 VDC     ■ 600 VDC     ■ 800 VDC

AMBIENT TEMPERATURE [°C]

■ 420 VDC    ■ 600 VDC    ■ 800 VDC

TECHNICAL DATA FRONIUS  SYMO (10.0-3-M, 12.5-3-M, 15.0-3-M, 17.5-3-M, 20.0-3-M)

| EFFICIENCY Max. efficiency European efficiency (ηEU) η at 5 % Pac.r 1) | SYMO 10.0-3-M SYMO 12.5-3-M 98.0 % | SYMO 15.0-3-M SYMO 17.5-3-M SYMO 20.0-3-M 98.1 % |
| --- | --- | --- |
|  | 97.4% 87.9 / 92.5 / 89.2 % | 97.6 % 88.7 / 93.1 / 90.1 % | 97.8 % 91.2 / 94.8 / 92.3 % | 97.8 % 91.6 / 95.0 / 92.7 % | 97.9 % 91.9 / 95.2 / 93.0 % |
| η at 10 % Pac.r 1) | 91.2 / 94.9 / 92.8 % | 92.9 / 96.1 / 94.6 % | 93.4 / 96.0 / 94.4 % | 94.0 / 96.4 / 95.0 % | 94.8 / 96.9 / 95.8 % |
| η at 20 % Pac.r 1) η at 25 % Pac.r 1) η at 30 % Pac.r 1) η at 50 % Pac.r 1) η at 75 % Pac.r 1) | 94.6 / 97.1 / 96.1 % 95.4 / 97.3 / 96.6 % 95.6 / 97.5 / 96.9 % 96.3 / 97.9 / 97.4 % 96.5 / 98.0 / 97.6 % | 95.4 / 97.3 / 96.6 % 95.6 / 97.6 / 97.0 % 95.9 / 97.7 / 97.2 % 96.4 / 98.0 / 97.5 % 96.5 / 98.0 / 97.6 % | 95.9 / 97.4 / 96.7 % 96.2 / 97.6 / 97.0 % 96.5 / 97.8 / 97.3 % 96.9 / 98.1 / 97.7 % 97.0 / 98.1 / 97.8 % | 96.1 / 97.6 / 96.9 % 96.4 / 97.8 / 97.2 % 96.6 / 97.9 / 97.4 % 97.0 / 98.1 / 97.7 % 97.0 / 98.1 / 97.8 % | 96.3 / 97.8 / 97.1 % 96.7 / 97.9 / 97.4 % 96.8 / 98.0 / 97.6 % 97.0 / 98.1 / 97.8 % 97.0 / 98.1 / 97.7 % |
| η at 100 % Pac.r 1) | 96.5 / 98.0 / 97.6 % | 96.5 / 97.8 / 97.6 % | 97.0 / 98.1 / 97.7 % | 96.9 / 98.1 / 97.6 % | 96.8 / 98.0 / 97.6 % |
| MPP adaptation efficiency | > 99.9 % |

| PROTECTIVE DEVICES | SYMO 10.0-3-M | SYMO 12.5-3-M SYMO 15.0-3-M SYMO 17.5-3-M | SYMO 20.0-3-M |
| --- | --- | --- | --- |
| DC insulation measurement |  | Yes |  |
| Overload behaviour |  | Operating point shift. power limitation |  |
| DC disconnector |  | Yes |  |
| Reverse polarity protection |  | Yes |  |
| INTERFACES | SYMO 10.0-3-M | SYMO 12.5-3-M SYMO 15.0-3-M SYMO 17.5-3-M | SYMO 20.0-3-M |
| WLAN / Ethernet LAN |  | Fronius Solar.web, Modbus TCP SunSpec, Fronius Solar API (JSON) |  |
| 6 inputs and 4 digital inputs/outputs |  | Interface to ripple control receiver |  |
| USB (A socket) 2) 2x RS422 (RJ45-socket) 2) Signalling output 2) Datalogger und Webserver External input 2) RS485 |  | Datalogging, inverter update via USB flash drive Fronius Solar Net Energy management (potential-free relay output) Included S0-Meter Interface / Input for overvoltage protection Modbus RTU SunSpec or meter connection |  |

1) And at Umpp min / Udc.r / Umpp max    2) Also available in the light version.

/ Perfect Welding / Solar Energy / Perfect Charging

WE HAVE THREE DIVISIONS  AND  ONE PASSION:  SHIFTING THE LIMITS OF POSSIBILITY.

/ Whether welding technology, photovoltaics or battery charging technology − our goal is clearly defined: to be the innovation leader. With around

3,300 employees worldwide, we shift the limits of what’s possible - our record of over 900 granted patents is testimony to this. While others progress step by step, we innovate in leaps and bounds. Just as we’ve always done. The responsible use of our resources forms the basis of our corporate policy.

Further information  about all Fronius products and our global sales partners and representatives  can be found at www.fronius.com

v05 May 2015 EN

Fronius India Private Limited GAT no 312, Nanekarwadi Chakan, Taluka - Khed District Pune 410501

India

pv-sales-india@fronius.com www.fronius.in

Fronius Australia Pty Ltd.

90-92 Lambeck Drive

Tullamarine VIC 3043

Australia

pv-sales-australia@fronius.com www.fronius.com.au

Fronius UK Limited Maidstone Road, Kingston Milton Keynes, MK10 0BD United Kingdom

pv-sales-uk@fronius.com www.fronius.co.uk

Fronius International GmbH

Froniusplatz 1

4600 Wels

Austria

pv-sales@fronius.com www.fronius.com

# Text boxes

EFFICIENCY [%]

OUTPUT POWER [W]

EFFICIENCY [%]

OUTPUT POWER [W]

EFFICIENCY [%]

OUTPUT POWER [W]

Text and images correspond to the current state of technolog y at the time of printing. Subject to modifications.

All information  is without guarantee in spite of careful editing - liability excluded. Copyright © 2011 Fronius™. All rights reserved.

M,06,0092,EN v16 Sep 2015   as17