® HIKRA

PRO

Our TÜV certified solar cable HIKRA® PRO meets the requirements of the DKE (German Electrical Commission) and features optimal mechanical and electrical properties. Robust  materials  defy  the  long-term  influences  of nature and offer a maximum of quality and safety.

HIKRA®PRO  is  made  for   outdoor  and  indoor  installation,  as   fixed

installation or steady movement in free motion.

► Features                                  UV-, ozone-, acid-, alkali- and weather-resistance

       Flame-retardant, halogen-free

       Good abrasion resistance, robust

       Highly flexible for high mechanical stress

       RoHS und REACH-conformant

       Sheath colours: black / red

 	25- years factory warranty from date of delivery. The warranty conditions for HIKRA® Pro cable apply for intended use, installation and operating conditions.

| ► Technical Data |   | Approvals TÜV 2 Pfg. 1169/08.07 (R 60079103) W orking temperature range: -40° C to +90° C ¦ Overload temperature: +120° C |
| --- | --- | --- |
|  |  | Minimum bending radius flexible ¦ fixed: 10 cable dia. ¦ 4x cable dia. |
|  |  | Short circuit temperature: Max 200°C 5S |
|  |   | Nominal voltage [U0/U]: AC 600 / 1.000 V ¦ DC 900 / 1.500 V Test voltage: AC 6,5 kV / DC 15 kV |
|  |  | Max. Voltage 1.800 V (conductor/conductor not grounded system, non-loaded circuit) |

► Construction                           Tin-plated copper strand, fine wire as per IEC 60228 class 5

       Double insulated

       Insulation / Chemically cross-linked special compound

Colour scheme

| Order No. | Sectionmm² | Conductor construction n xmax-ø (mm) | Maximumof conductor resistance (Ω/km) | External diameter (± 0,2 mm) | Weight, approx. kg/km |
| --- | --- | --- | --- | --- | --- |
| black | red |  |  |  |  |  |

725213       725255           1 x 2,5            48 x 0,25                8,21                         5,0                        40

| 725214 725257 1 x 4,0 52 x 0,30 5,09 5,3 60 |
| --- |
| 725215 725258 1 x 6,0 76x 0,30 3,39 | 5,8 80 |
| 725216 725259 1 x10,0 78 x 0,40 1,95 6,9 140 |

725217       725260          1 x16,0          118 x0,40                1,24                         8,3                       198

HIS Renewables GmbH Siemensstraße 4

64743 Beerfelden

Tel. +49 6068 9314 400

Fax +49 6068 9314 411 info@his-solar.de

www.his-solar.com

Stand: 25.03.2013/HO-af